## Slide 1: COMPUTER ARCHITECTURE
The relationship between hardware (stuff you can touch) and software (programs, code). I can design a computer that has hardware which executes programs in any programming language. For example: a computer that directly executes Pascal.
we do just that:
1. From experience (in the engineering community), we know that the hardware that executes HLL programs directly are slower than those that execute a more simple, basic set of instructions.
2. Usability of the machine. Not everyone wants a Pascal machine. ANY high level language can be translated into assembly language.

## Slide 2
In whatever language you are writing programs, it will look like you have a machine that executes those programs directly.
BASIC COMPUTER OPERATION
Simplified diagram of a computer system (hardware!)
------- ----------
| CPU | <---------> | memory |
------- | ----------
|
|
-------
| I/O |
-------

## Slide 3
CPU -- controls the running of programs, executes instructions, makes requests of the memory. CPU stands for central processing unit.
CPU and processor are synonyms (book uses the term processor)
Memory -- where programs and program variables are stored, handles requests from the CPU

## Slide 4
Fetch and execute instruction
How does the CPU execute a program ? CPU executes a program by repeatedly fetching one instruction from memory and executing the instruction in an endless cycle called the Fetch/ Execute Cycle.
To execute a program , CPU implements this cycle in five steps as below:
General Fetch/ Execute
1. Initialize CPU
2. Fetch instruction at IP (PC)
3. PC = next instruction address
4. Decode instruction OP
5. Execute operation OP
**Intel calls PC an IP, others call it PC